## Slide 1: Physically-Augmented Design: Step 1
Steve Hoover
July, 2011

## Slide 2: Outline
  Background
  Today’s design process and its challenges (the problem)
  PAD Methodology overview (the solution)
  Step 1: System Verilog Extension (SVX)
    examples
  Closing thoughts

## Slide 3: Background
  HLM is good… but so many failures. Why?
    Additional languages/models
    No validation path to RTL
    Loss of control over implementation
    Benefits outweighed by new overhead
  Working group in Hudson led to PAD concept, drawing from many past efforts (2005/2006)
  Paper presented externally (2008)
  Significant interest from various parties throughout Intel, but no serious investment… till now!
  Recently, I defined a subset, called SVX, for use on my current from-scratch logic.
  Project and division have approved SVX to be developed (as open source) and deployed.

## Slide 4: Outline
  Background
  Today’s design process and its challenges (the problem)
  PAD Methodology overview (the solution)
  Step 1: System Verilog Extension (SVX)
    examples
  Closing thoughts

## Slide 5: Models and Mappings
Validation
Models
aRTL
SDP
Layout
RLS
Abstract
Human
Tool
Validation
Notes: Develop and maintain many models and many mappiings.
Tools validate Layout vs. sch. vs. RTL.
Functional and formal validation of RTL. Significant effort.

## Slide 6: Physical Impact
Validation
Models
sRTL
Abstract
Human
Tool
SDP
Layout
RLS
Validation
Notes: RTL is a moving target for val models; complexity in mappings.
Greater detail -> more bugs and debug effort.
Phys changes require regression.
Abstraction is lost. Hard to reverse-engineer; phys baggage (RTL & val) from the start.

## Slide 7: Validation Models
Queuing
Mdels
RTL
HLM
X-Actors
Ref. Models
ISA/
Mem. Order
Protocol
Models
MAS
Perf.
Model
uArch
Concept
Visualization
Coverage
SDP
Layout
RLS
Notes: Many validation models with mappings to RTL that must be maintained as aRTL becomes sRTL.

## Slide 8: Outline
  Background
  Today’s design process and its challenges (the problem)
  PAD Methodology overview (the solution)
  Step 1: System Verilog Extension (SVX)
    examples
  Closing thoughts

## Slide 9: PAD Methodology
Validation
Models
sRTL
Behavior
PAD
Code
Validation
Layout
SDP
RLS
Notes: We propose introducing a logical RTL model that is detached from its physical implementation and is maintained throughout the project.
We propose capabilities to map the aRTL to sRTL.
Mapping capabilities include isolated bits of sRTL with formal and functional validation path.
The mapping absorbs much of the implementation churn and mapping changes are lighter weight – they do not require regression simulations.
Functional validation against a simpler more stable target.

## Slide 10: Mappings
PAD Behavioral Spec
Pipeline
Staging
01101
Physical
Partitioning
opcode = read
Encoding

## Slide 11: Refinement
head
tail
Abstraction
Refinement

## Slide 12: Outline
  Background
  Today’s design process and its challenges (the problem)
  PAD Methodology overview (the solution)
  Step 1: System Verilog Extension (SVX)
    examples
  Closing thoughts

## Slide 13: SVX PAD Subset (for HSX+ EDC)
  In:
  Auto clock gating
  X’s in traces
  Free vars in abstractions
  Assumptions in abstractions
  Half-clock
  Syntactic fluff
opcode = read
01101
  Out:
  FV of refinements
  Elimination of regression testing
  Generic component support

## Slide 14: Data Flow Model
  Pipelines/Transactions:
    Pipelines are non-backpressured conduits for transactions.
    Transactions may pass through multiple pipelines and storage structures.
    A field ($name) of a transaction in a pipeline corresponds to a signal physically, and may have multiple staged versions physically.
  Validity:
    Established via “>When …” block.
    Generally, contents of “>When …” can be thought of as a transaction within a pipeline.
    Invalid logic may not be consumed by valid logic (implicit assertions).
    Simulation can generate Xs for invalid – useful in trace debug.
    Clock gating logic can be generated or validated.
  State variables:
    State vars retain their value (by default) over invalid cycles.
    State vars have reset values.

## Slide 15: Outline
  Background
  Today’s design process and its challenges (the problem)
  PAD Methodology overview (the solution)
  Step 1: System Verilog Extension (SVX)
    examples
  Closing thoughts

## Slide 16: SVX Example
|issue
/inst[3:0]
@0
$valid = …;
>When $valid
@1
$mem_op = $raw_inst[28:27] == 2’b01;
>When $mem_op
@3
$mem_addr[50:0] = $op_a + $raw_inst[15:0];
issue
inst
1
2
3

## Slide 17: SVX Example
|issue
/inst[3:0]
@0
$valid = …;
>When $valid
@1
$mem_op = $raw_inst[28:27] == 2’b01;
>When $mem_op
@3
$mem_addr[50:0] = $op_a + $raw_inst[15:0];
// |issue
for (int inst = 0; inst < 4; inst++) begin
// @0
always_comb Issue_Inst_valid_u100H[inst] = ...;
// >When $valid
// @1
always_comb Issue_Inst_mem_op_u101H[inst] = Issue_Inst_raw_inst_...
// >When $mem_op
// @3
always_comb Issue_Inst_mem_addr_u104H[50:0][inst] =
Issue_Inst_op_a_u104H[inst] + Issue_Inst_raw_inst_...; end

## Slide 18: SVX Example (Continued)
// Signal Declarations
//
// Primary signals
node Issue_Inst_valid_u100H[3:0];
node Issue_Inst_mem_op_u101H[3:0];
node [50:0] Issue_Inst_mem_addr_u103H[3:0];
// Staged signals
node Issue_Inst_valid_u101H[3:0];
node Issue_Inst_mem_op_u102H[3:0];
node Issue_Inst_mem_op_u103H[3:0];
node [15:0] Issue_Inst_raw_inst_u102H[3:0];
node [15:0] Issue_Inst_raw_inst_u103H[3:0];

## Slide 19: SVX Example (Continued)
// Clock gating
//
// For ck_Issue_Inst_valid_1_u1n44[3:0]
node ck_Issue_Inst_valid_1_u1n44[3:0];
for (int inst = 0; inst < 4; inst++) begin
`MAKE_CLK_LOC(ck_Issue_Inst_valid_1_u1n44[inst], ck_grid_u1n22, 1'b1,
Issue_Inst_valid_u100H[inst], csr_pwrdn_ovrd_unnnH)
end
// For ck_Issue_Inst_valid_And_mem)op_2_u1n44[3:0]
node Issue_Inst_valid_And_mem_op_u101H[3:0];
node ck_Issue_Inst_valid_And_mem_op_2_u1n44[3:0];
for (int inst = 0; inst < 4; inst++) begin
Issue_Inst_valid_And_mem_op_u101H[inst] = Issue_Inst_valid_u101H[inst] &&
Issue_Inst_mem_op_u101H[inst];
`MAKE_CLK_LOC(ck_Issue_Inst_valid_And_mem_op_2_u1n44[inst], ck_grid_u1n22,
1'b1, Issue_Inst_valid_And_mem_op_u101H[inst],
csr_pwrdn_ovrd_unnnH)
end

## Slide 20: SVX Example (Continued)
// Clock gating (continued)
//
// For ck_Issue_Inst_valid_And_mem_op_3_u1n44[3:0]
node Issue_Inst_valid_And_mem_op_u102H[3:0];
node ck_Issue_Inst_valid_And_mem_op_3_u1n44[3:0];
for (int inst = 1; inst < 4; inst++) begin
`MSFF(Issue_Inst_valid_And_mem_op_u102H, Issue_Inst_valid_And_mem_op_u101H,
ck_grid_u1n22)
`MAKE_CLK_LOC(ck_Issue_Inst_valid_And_mem_op_3_u1n44, ck_grid_u1n22, 1'b1,
Issue_Inst_valid_And_mem_op_u102H, csr_pwrdn_ovrd_unnnH)
end

## Slide 21: SVX Example (Continued)
// Staging flops (some gated)
//
for (int inst = 0; inst < 4; inst++) begin
`MSFF(Issue_Inst_valid_u101H[inst], Issue_Inst_valid_u100H[inst],
ck_grid_u1n44);
`MSFF(Issue_Inst_mem_op_u102H[inst], Issue_Inst_mem_op_u101H[inst],
ck_Issue_Inst_valid_And_mem_op_u102H[inst])
`MSFF(Issue_Inst_raw_inst_u102H[inst][15:0],
Issue_Inst_raw_inst_u101H[inst][15:0],
ck_Issue_Inst_valid_And_mem_op_u102H[inst])
end

## Slide 22: SVX Example Comments
  Code reduction from:
    Scope (hierarchy, pipeline, pipestage, clock gating) applied to multiple lines/signals
    Implicit signal declarations
    Implicit staging flops
    Generated clock gating logic
  Debug:
  SVX: |issue /inst[*] @3 >Expose $*
Issue_Inst_*_u103H[0]*
Issue_Inst_valid_u103H[0]
Issue_Inst_mem_op_u103H[0]
Issue_Inst_raw_inst_u103H[0][31:0]
0x2f046820
/////////////////////////////
//////////////
//////////////
//////////////

## Slide 23: Timing Abstraction
1: |inst 2: @3 3: $a_op = select 4: $imm_a : $imm_data 5: $byp_a : $rslt#+1 6: $reg_a : $reg_data#+2 7: $mem_a : |mem$mem_data#+5;
$reg_data
$rslt
$imm_data
$mem_data
$a_op
|inst
|mem
3
4
5
6
7
5
8
4
2
9
+

## Slide 24: Timing Abstraction
$reg_data
$rslt
$imm_data
$mem_data
$a_op
|inst
|mem
+
3
4
5
6
7
5
8
4
2
9
1: |inst 2: @4 3: $a_op = select 4: $imm_a : $imm_data 5: $byp_a : $rslt#+1 6: $reg_a : $reg_data#+2 7: $mem_a : |mem$mem_data#+5;

## Slide 25: Outline
  Background
  Today’s design process and its challenges (the problem)
  PAD Methodology overview (the solution)
  Step 1: System Verilog Extension (SVX)
    examples
  Closing thoughts

## Slide 26: Topics for Another Day
  Refinements
    Examples
    Keeping abstractions abstract with assumptions
    Breaking the shackles of cycle accuracy with free variables
  PAD topics not addressed by SVX:
    Encoding abstraction
    Modes and transitions
    Formal validation opportunities
    Opportunities for PAD-aware simulation and debug
    Hardware emulation
    Integration of performance modeling
  What's after SVX?

## Slide 27: Acknowledgements
PAD/SVX is a culmination of many ideas that have existed within Intel and throughout our industry in various forms over many years. Thanks, to all who have pursued and are pursuing them.