## Slide 1: SVX as it Relates to Simulation Speed
Steve Hoover
Q4 2012

## Slide 2: Outline
Physically Augmented Design (PAD)
  Simulation Speed Implications of PAD
SVX Status
  Simulation Speed Implications of SVX Today
Next Step: Abstractions/refinements
  Simulation Speed Implications of Abstractions
Tacked-on comments about build speed

## Slide 3: Models and Mappings
Validation
Models
aRTL
Schematics
Layout
Synthesis
Abstract
Human
Tool
Validation
Notes: Develop and maintain many models and many mappiings.
Tools validate Layout vs. sch. vs. RTL.
Functional and formal validation of RTL. Significant effort.

## Slide 4: Physical Impact
Validation
Models
sRTL
Abstract
Human
Tool
Schematics
Layout
Synthesis
Validation
Notes: RTL is a moving target for val models; complexity in mappings.
Greater detail -> more bugs and debug effort.
Phys changes require regression.
Abstraction is lost. Hard to reverse-engineer; phys baggage (RTL & val) from the start.

## Slide 5: Physical Impact
Validation
Models
sRTL
Abstract
Human
Tool
Schematics
Layout
Synthesis
Behavior
PAD
Code
Validation
Notes: RTL is a moving target for val models; complexity in mappings.
Greater detail -> more bugs and debug effort.
Phys changes require regression.
Abstraction is lost. Hard to reverse-engineer; phys baggage (RTL & val) from the start.

## Slide 6: Validation Models
Queuing
Mdels
RTL
HLM
X-Actors
Ref. Models
ISA/
Mem. Order
Protocol
Models
MAS
Perf.
Model
uArch
Concept
Visualization
Coverage
Schematics
Layout
Synthesis
Notes: Many validation models with mappings to RTL that must be maintained as aRTL becomes sRTL.

## Slide 7: Mappings
PAD Behavioral Spec
Pipeline
Staging
01101
Physical
Partitioning
opcode = read
Encoding

## Slide 8: Refinement
head
tail
Abstraction
Refinement

## Slide 9: Refinement
head
tail
Abstraction
Refinement
Refinements provide a general abstraction mechanism to go beyond mappings.
Refinements range from tiny to huge
  Huge: big array w/ bypass network, sectoring, DFX, error correction, etc.) (8K lines -> 200)
  Tiny: A single behaviorally-atomic expression can be split across pipestages w/ a refinement.
Enables a divide and conquer approach to validation.
  Validate refinement == abstraction formally or via shadow simulation.
  Validate abstraction in simulation.
Debug focuses on abstractions, except shadow simulation mismatches, which are localized to the refinement.
More to come on the challenges and solutions w/ refinements…

## Slide 10: PAD Implications for Simulation Speed
Abstract models simulate faster!
PAD provides abstraction w/o an additional model and language in the design process.
There is NO loss in integrity due to abstraction (except where desired).
Abstract models occupy less emulator hardware.
Abstract models build faster -> more feasible to target to emulation.
More feasible to build different models w/ different components abstracted (behaviorally-approximate and behaviorally-aggressive). Again, smaller models; faster build.
PAD enables architectural exploration and performance modeling in the same infrastructure. Following this approach, abstractions are available and validated prior to FED. This means fewer bugs and enables smaller models for FED/EXE, which means less simulation.

## Slide 11: SVX Example
\SVX
|issue ^clock=“C” ^pipe=6
>inst[3:0]
@0
$valid = *valid_U600H[inst];
?valid
@1
$mem_op = $raw_inst[28:27] == 2’b01;
?mem_op
@3
$mem_addr[50:0] = $op_a + $raw_inst[15:0];
issue
inst
1
2
3
==
+
raw_inst

## Slide 12: Retiming Made Easy in SVX: Operand MUX Example
|inst
|mem
@9
@6
@5
@4
@3
@8
@7
@6
mux
$mem_data
$reg_data
$rslt
1: |inst 2: @3 3: $a_op[63:0] = 4: $byp_a ? $rslt#+1 : 5: $reg_a ? $reg_data#+2 : 6: $imm_a ? $imm_data : 7: $mem_a ? |mem$mem_data#+5 : 8: 64’b0;
@4
$a_op
mux
@3
@2
$imm_data
In SVX, this change impacts 1 character of code, and is functionally-safe.
In SV, this change impacts ~15 lines of code, w/ risk of functional bugs.

## Slide 13: Timing Abstraction Simulation Speed Implications
Can experiment w/ SV code constructs w/o source code changes via preprocessor changes.
Knowledge of validity enables aggressive X injection and aggressive clock gating which can avoid simulation events and _might_ simulate faster.
Logic can safely be retimed to produce a simulation-optimized model
  Valid conditions computed early. Simulate w/ behavioral valid condition, not physical gaters.
  Minimize number of flops.
Timing-isolation of validation collateral (including emulation monitors)
  SVX provides staging to align fields of transaction.
  SVX has knowledge of validity, so it knows when transaction is available to communicate w/ hardware emulator.
More practical to write synthesizable validation collateral (and assertions)
  For hardware emulation
  To eliminate SV <-> C++ overhead
  To empower logic designers to write “validation” code

## Slide 14: Beyond Complete, Cycle-Accurate Abstractions
Abstraction is hard because…
  Implementation details become exposed in behavior, esp. via DFX hooks.
Addressed with
  Free variables
  Assumptions
  Invalidity (?when)

## Slide 15: (Constrained) Free Variables (1)
We can do a lot with cycle-accurate abstractions. Introducing free variables takes us to the next level of abstraction.
An assignment statement in an abstraction can define the set of legal values for a pipesignal. This is done by assigning a decoded signal, where each bit represents whether the corresponding value is legal.
So, where does the choice come from in simulation? It can be configured at runtime to be provided by:
  The refinement if it is present and enabled (shadow simulation) and contains a corresponding pipesignal
  A legal choice is provided by generated pseudo-random instrumentation code, or
  A choice is provided by validation collateral and checked; or a restriction of choices is provided and pseudo-random instrumentation code provides the final choice
One free variable’s constraints can depend on another’s choice. For example, if the choice of issue instruction was not a branch, the choice of prediction must be not-taken. There’s nothing special to enable this, but validation collateral providing values must be aware of dependencies and the ordering of their evaluation in simulation.
Removes non-functional (policy/prediction) decisions from behavioral spec.

## Slide 16: (Constrained) Free Variables (2)
FEV requires corresponding pipesignal in refinement to provide input to free variable. Assertion ensures that refinement’s choice is legal. FEV ensures that refinement implements abstraction if the choice is legal. Assertion proves choice is legal, via formal validation or shadow simulation.
Increases validation space, but enables validation of the design as it was intended to function, unconstrained by real choices; once this space is validated, the policy decision can be changed safely.
Enables easier/better coverage of corner cases; for example, it’s difficult to replace a cache line that was just filled without this.
Important enabler for abstractions to remain abstract

## Slide 17: Abstractions as Reference Models
Incorporating free variables into abstractions is analogous to extending a shadow model to make it a reference model/checker. While a traditional reference model/checker checks that the observed behavior is legal, an abstraction with free variables on its outputs specifies the set of legal behaviors, and outputs are verified to be among them.
Versus a traditional reference model/checker, an abstraction with free outputs:
  Serves as the first simulate-able model
  Serves as the target of functional debug
  Has known complete checking over a clear boundary; holes manifest as bugs, not non-bugs
  Is synthesizable
  Can be exposed to formal validation

## Slide 18: Abstractions as Transactors
An abstraction of “the rest of the system” is analogous to a transactor.
Defines legal inputs via constrained free variables.
Enables formal validation by providing input constraints.
Enables dynamic validation w/ (untuned) random stimulus.
Transactors can provide tuned free variable inputs and can be checked by abstraction.
Good framework for Unit-Level Testing.

## Slide 19: Assumptions
Abstractions can be valid under given assumptions
Eg: If CSR config is set, the behavior is… or, as long as BIST isn’t run, the behavior is… or, as long as there’s no reset after the first transaction, the behavior is…
Tests state their assumptions via deposits to instrumentation signals which disable abstractions and enable refinements (which requires that they have been built) as appropriate
Assumptions that are violated report non-fatal error and disable abstractions
Important enabler for abstractions to remain abstract

## Slide 20: Knowledge of Invalid Transactions
?when construct is useful in many ways… one of which is that there is no need for the abstract and refined models to match on invalid outputs.

## Slide 21: Simulation Speed Implications of Abstractions
Contributes to ease of use of ULT. Try formal first; if intractable, try automated dynamic content; if insufficient, tune stimulus (free variable choices) – all from the same collateral. ULT means less simulation/smaller models.
Smaller and more abstract models

## Slide 22: Capacity
Abstractions do not fundamentally reduce the amount of state in the model.
In fact, in some cases they increase it
  You might want an abstract FIFO with unbounded size to cover various possible implementations. This is not synthesizable and isn’t allowed, so you create a sufficiently large one. This is bigger than the refinement.
  Where shadow modeling, both abstraction and refinement (plus checking) exist.
  Additional instrumentation logic for stimulus of free variables.
However, it’s easier to parameterize an abstract model, and refinements make it easier to create minimal-capacity simulation-optimized variants. This can significantly further reduce model sizes.

## Slide 23: PAD Implications for Build Time (tacked-on)
Today’s SVX:
  Light-weight preprocessor -- little impact to successful builds.
  Fast filter for some errors.
  No errors in generated code, so fewer builds to get it right.
PAD:
  Different builds for validation and phys. Phys builds would be comparable to today’s.
  More models to build, but smaller models.
  FEV could be part of build.
  Deltas in mappings and refinements do not require rebuild/regress. Can be done by phys team.
  Good build caching very important/valuable.