## Slide 1: Considerations
Version control, build flow, and build overhead
Building what we are validating
Model configurations
Use of SV content in SVX (includes shared macros, modules, and functions; RFs; CSR collateral; and leveraged code)
Clock gating
eclk/ehclk
Clock crossings
FUB (& section/chip) boundaries
Backend flows (Scan/SROSL insertion, shark, syncs, etc.)
Relating SV debug to SVX
Vaildation ports to SV (incl. coverage and sigmap use)
Hardware emulation – leveraged RTL solution for EDRAM. Benefit for tag array
Legacy impact
Risk mitigation
Staging plan (esp. feature enablement and phys enablement -- loose decoupling of phys and val.)

## Slide 2: Building What We Are Validating
Instrumentation code for:
  Abstractions (abstract side of refinements)
  Timing-abstract validation ports
  Assertions
  Assumption checking and disabling of abstractions
  Driving X’s (only in abstractions)
All instrumentation code is buried in a single module with no outputs. #ifdef inst_on around module instantiation.
Replaces hand-generated instrumentation code (esp. assertions), so less risk.

## Slide 3: Model Variants
Preprocessor options (flavors of generated code)
  For early development and debug optimization w/ focus on abstraction
    Can elect to have abstractions drive downstream logic (all, or select refinements) when low confidence in refinement(s). Refinement bugs are non-blocking.
    Can omit refinements (if known-broken, for faster simulation, or to enable control over free variables)
    Can use X’s aggressively (not limited to abstractions). Cleaner traces, though some SV code obscurity
  For SVX abandonment
    Max readability/maintainability
    No ‘line and line alignment of SV vs. SVX
    Aggregation of always_comb
  SVX behavioral filter
    Filter all physical elements, leaving behavioral elements only (output is SVX, no SV)
    Starting point for reverse engineering
    Basis for comparing changes at a behavioral level

## Slide 4: Free Variables (back)
Generally, we target cycle-accurate abstractions, but free variables can provide further abstraction
If not all values are legal, instrumentation logic defines set of legal values for a pipe signal
One free variable’s constraints can depend on another’s choice (nothing special to enable this) (For example, if the choice of issue instruction was not a branch, the choice of prediction must be not-taken.)
Choice is provided by the refinement if present, or a legal choice is provided by generated pseudo-random instrumentation code, or choice is provided by validation collateral and checked
Removes non-functional (policy/prediction) decisions from behavioral spec.
Increases validation space, but enables validation of the design as it was intended to function, unconstrained by real choices; once this space is validated, the policy decision can be changed safely.
Enables easier/better coverage of corner cases; for example, it’s difficult to replace a cache line that was just filled without this

## Slide 5: Free Variables (2)
Incorporating free variables into abstractions is analogous to extending a shadow model to make it a reference model/checker. While a traditional reference model/checker checks that the observed behavior is legal, an abstraction with free variables on its outputs specifies the set of legal behaviors, and outputs are verified to be among them.
Versus a traditional reference model/checker, an abstraction with free outputs:
  Serves as the first simulate-able model
  Serves as the target of functional debug
  Has known complete checking over a clear boundary; holes manifest as bugs, not non-bugs
  Is synthesizable
  Can be exposed to formal validation

## Slide 6: Assumptions (back)
Abstractions can be valid under given assumptions
Eg: If CSR values are xxx, the behavior is… or, as long as BIST isn’t run, or as long as there’s no reset after the first transaction, the behavior is…
Tests state their assumptions via writes to instrumentation signals which disable assertions
Assumptions that are violated report non-fatal error and disable abstractions
No abstraction benefit outside of assumptions
Important enabler for abstractions to remain abstract

## Slide 7: Hard Reuse/Leverage and Shared Code (back)
Covers shared or leveraged macros, modules, and functions such as RFs, CSR collateral, shared kernels, etc.
SV can be mixed freely with SVX
Macro, module, and function instantiations can use pipe signals
Statements using SV signals are not timing-abstract
No perceived need for SVX-native generic programming, macros, parameterization for EDC deployment

## Slide 8: Clock Gating (back)
All clock gating logic is auto-generated and correct-by-construction (verified in simulation)
Clock gating condition is transaction valid condition or an explicit superset condition that is validated with a generated assertion
RCB gating not important for EDC, so just LCB supported (but could support RCB gaters), and SV can use custom gating

## Slide 9: Validation’s Connection w/ SVX Code
Validation (including coverage) mostly maps into abstract model
Explicit list of validation-driven/-consumed signals
  SVX can generate required staged (or anti-staged) versions of pipe signals.
  SVX can report a broken validation dependency for a logic change quickly (vs. pre-simulation check failure).
Validation collateral will connect to generated instrumentation SV signals; can access raw signals, but lose abstraction benefits

## Slide 10: Pre-loading/Injection
Must pre-load/inject both models
Abstract is generally much less effort
Can often inject outside of refinements

## Slide 11: Relating SV Debug to SVX (back)
Problem: Error messages and debug at source level (Verdi) must be related back to SVX
Use `line directive intended for this purpose
Must investigate Verdi support
Backup plan: maintain strict line alignment

## Slide 12: Hardware Emulation
SVX viewed as a small benefit
Plan to use abstract tag array on emulator, eliminating custom emulator variant of tag array
Consideration given to assumptions of abstract tag array to be sure we can support flows like POST on emulator. We can.
Other abstractions can be used on emulator, either to reduce the model or to get shadow-checking benefits, but the perceived benefit is small

## Slide 13: Unwritten Code
Special syntax for unwritten code (undriven signal) that is recognized by SVXpp
Can be used in refinement/abstraction tagged as “incomplete”
Useful for
  tracking to-do’s
  providing early phys-targeted refinements that are functionally incomplete

## Slide 14: Legacy Impact (back)
Plan for abandonment. Preprocessor generates readable/maintainable output; any surprises will be brought to WG
Abstractions are part of the leveraged source and are required to the extent that leveraged validation collateral is tied to them; can consider them to be part of leveraged validation collateral
Leveraging projects will see a reverse-engineering benefit and code structure benefit even if SVX is abandoned