## Slide 1: SVX Data Flow
Steve Hoover
Aug 2013

## Slide 2: Agenda
Transaction-Level Modeling in SVX
The meaning of X
Examples
  Toy Ring
  Pipeline logic
  Latch-based pipeline (Synchronous ELastic Flow – SELF)
Takeaway

## Slide 3: Transactions and Data Flow in SVX
Logic is expressed in the context of transactions which traverse pipelines and flows
SVXpp manages the staging/progression of signals through the pipelines/flows as required based on producing/consuming stages. SVXpp generates all flops/latches
Transaction flow can be expressed independently from the logic of the transaction
Transaction flow can be defined in libraries that are independent of the transaction logic that occurs within the flow. Note that generic library capabilities are purely proof-of-concept at this point and are not recommended for broad deployment.
Flow elements include FIFOs, queues, arbiters, back-pressure, bypass, etc.
The transaction logic is bucketed to pipelines and pipestages defined by the flow; logic can be re-bucketed w/ no impact to behavior

## Slide 4: Flow Example
FIFO
QUEUE
Bypass
free-flow
pipeline
backpress.
pipeline
free-flow
pipeline
comb
Transaction Logic
comb
comb
comb
comb
comb
comb
free-flow
pipeline
comb
0
bypass

## Slide 5: Mapping Logic to Pipeline/Pipestage
FIFO
QUEUE
Bypass
free-flow
pipeline
backpress.
pipeline
free-flow
pipeline
free-flow
pipeline
comb
comb
comb
comb
comb
comb
comb
comb
0
bypass

## Slide 6: Design Changes
FIFO
QUEUE
Bypass
free-flow
pipeline
backpress.
pipeline
free-flow
pipeline
free-flow
pipeline
comb
comb
comb
comb
comb
comb
comb
comb
0
bypass

## Slide 7: Design Changes
FIFO
QUEUE
Bypass
free-flow
pipeline
backpress.
pipeline
free-flow
pipeline
free-flow
pipeline
comb
comb
comb
comb
comb
comb
comb
comb
0
bypass
Old FIFO contents
New FIFO contents

## Slide 8: Proof of Concept for Library Development in SVX
M4 macro-preprocessor in front of SVX
  Provides easy solution for parameterization, replication, etc.
  Not a long-term solution; very messy syntax
  Provides proof-on-concept prior to native SVX language features
Created back-pressured pipeline
  Each stage of the pipeline is a unique SVX (non-backpressured) pipeline
  Signals pulled from one stage/pipeline to the next through a gated flop or recirculating mux as needed by the transaction logic.
  This is done with wildcarded signals ($ANY) as inputs/outputs of SV expressions. Eg:
  which says, recirculate the transaction from the previous cycle, or accept the transaction from the previous stage. (Granted, I haven’t explained the syntax.)
  These expressions construct a data flow graph which could be searched to find and pull transaction fields (signals) through the flow.

## Slide 9: Performance Modeling in SVX
SVX data flow makes it feasible to create concise abstract models
Models are synthesizable, enabling emulation of abstract models
Other SVX capabilities, not discussed in this presentation, assist in bridging the gap between abstract and RTL details
This enables a radical methodology change where performance models and models for architectural exploration could exist as part of the same code pool that provides RTL
Perf/arch models evolve into RTL
Validation is enabled earlier
Perf models and RTL are better aligned
Mix and match of “RTL” and perf components makes it easier to isolate the performance contributions of different “RTL” components

## Slide 10: Agenda
Transaction-Level Modeling in SVX
The meaning of X
Examples
  Toy Ring
  Pipeline logic
  Latch-based pipeline (Synchronous ELastic Flow – SELF)
Takeaway

## Slide 11: Don’t-Care Injection w/ SVX
Xs have two meanings:
  Don’t-Know: We don’t know what value the signal has. Could be 0 or 1.
  Don’t-Care: It doesn’t matter what value the signal has. Not visible impact either way.
If we Don’t-Know, we must ensure that we Don’t-Care – that’s what determinism validation is all about.
SVX makes it easy to provide Don’t-Care information as a reflection of design intent. Eg: fields of an invalid transaction.
SVXpp can generate SV code capable of injecting Don’t-Cares.
  Catch violations of design intent that would otherwise go undetected because they don’t manifest as real functional bugs.
  Filter out noise for debug (next 2 slides).

## Slide 12: Determinism Validation
Determinism validation ensures that Don’t-Know initial states are eliminated by cold reset (and are therefore Don’t-Cares).
With no distinction in simulation between Don’t-Know and Don’t-Care, X-injection for Don’t-Cares would get in the way of determinism validation, so it is disabled.
In other 4-state simulations, Xs are Don’t-Cares and X-injection is enabled. X-propagation ensures that Don’t-Cares really do not get consumed.

## Slide 13: Agenda
Transaction-Level Modeling in SVX
The meaning of X
Examples
  Toy Ring
  Pipeline logic
  Latch-based pipeline (Synchronous ELastic Flow – SELF)
Takeaway

## Slide 14: Ring Example
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid

## Slide 15: Ring code (expanded from invocation)
backpressure
data
valid
dest
valid
data
dest
data
valid
>stop[*]:
|rg
|fo
|ou
@0
@1
@2

## Slide 16: Simulation

## Slide 17: Ring + FIFOs
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
backpressure
data
valid
dest
valid
data
dest
data
valid
(fllop-based, w/ bypass
and single encoded
head/tail pointer mask)

## Slide 18: Ring + FIFOs SVX Code w/ SV Hookup
SV I/O hookup
Ring/FIFO instantiation

## Slide 19: Scenario
Silent data corruption too high, determined late in the project
Decide to cover complete data path through FIFOs and ring with single parity bit. Generate parity prior to FIFO, check at ring egress.
Extra cycle required for parity generation.

## Slide 20: Ring + FIFOs SVX Code w/ SV Hookup
~1 minute to modify & debug (addition of parity signal, not parity logic)
vs. ~100 lines of RTL change in generated RTL – bugs, bugs, bugs if done by hand!!!
Code change:
add $parity = …;
add $error = … $parity …;
0 → 1 (to feed FIFO 1 cycle later)
@1 (to consume backpressure 1 cycle later) (caught by SVXpp)

## Slide 21: Agenda
Transaction-Level Modeling in SVX
The meaning of X
Examples
  Toy Ring
  Pipeline logic
  Latch-based pipeline (Synchronous ELastic Flow – SELF)
Takeaway

## Slide 22: Pipeline Logic
decode
decode
data
decode
backpress.
data
decode
data
decode
data
decode
data
decode
data
decode
data
decode
data
decode
data
en
valid.
backpress.
en
valid.
backpress.
en
valid.
backpress.
en
valid.
backpress.
en
valid.
bypass
swizzle
data
backpress.
en
valid.
convert

## Slide 23: Pipeline Logic (implementation)
decode
data
decode
data
decode
backpress.
data
decode
data
decode
data
decode
data
decode
data
decode
data
decode
data
decode
data
en
valid.
backpress.
en
valid.
backpress.
en
valid.
backpress.
en
valid.
backpress.
en
valid.
swizzle
backpress.
en
valid.
convert

## Slide 25: Agenda
Transaction-Level Modeling in SVX
The meaning of X
Examples
  Toy Ring
  Pipeline logic
  Latch-based pipeline (Synchronous ELastic Flow – SELF)
Takeaway

## Slide 26: Synchronous ELastic Flow (SELF)
Design style explored by Michael Kishinevsky, et. al., in Intel’s Strategic CAD Lab
In SELF, transactions flow through pipelines that are backpressured at each latch, not at each flop, allowing each latch to hold a transaction, providing ~2x capacity
Abandoned several years ago, mainly because it was hard to migrate existing RTL to SELF
With SVX this would be the flick of a switch
Created a proof-of-concept SELF pipeline
(It’s actually the same code used to create the flop-based backpressured pipeline, using M4 to parameterize)

## Slide 27: Data flowing through a SELF pipeline

## Slide 28: Code (w/o explanation)
This is the complete code and testbench generating the previous waveform (excluding generic library code and clock/reset inputs)
Testbench
Transaction In
Transaction
Out
Logic

## Slide 29: Pipeline Example and SELF
Conversion to SELF pipeline trivial in SVX (w/ M4 library)
Just change this instantiation:
m4_bp_pipeline(S, S0, 1, 1, 8)
To this:
m4_self_pipeline(S, S0, 1, 1, 8)
Transparency can be used to reduce latency (by moving A-phase instantiations to B-phase).
Provides 5 free cycles of backpressure storage, deemed beneficial by designer.
Note that SELF has implication to SCAN methodology w/ 2 states per “flop”.
Note that this example has not been synthesized, just simulated.

## Slide 30: Agenda
Transaction-Level Modeling in SVX
The meaning of X
Examples
  Toy Ring
  Pipeline logic
  Latch-based pipeline (Synchronous ELastic Flow – SELF)
Takeaway

## Slide 31: Takeaway
Logic design does not have to be a painful experience 
Significant potential today, w/ small fraction of envisioned feature set.
Huge potential benefit w/ more investment.
We’re past the initial hump. An hour of investment will save more than an hour of project effort… on one project alone.
Need:
  Investment
  Industry/academic collaboration, open-sourcing
  You!